## Slide 1
2.4 Boolean logic | Lesson 3
Circuit workshop
Engineers turn real problems into logic. In the workshop you'll read three scenarios, build the circuit for each one, and complete its truth table.
OCR J277 Paper 2 | Computational thinking, algorithms and programming
Notes: Lesson 3: Circuit workshop. Open the experience at revise360.co.uk and hand out BL_L03_CircuitWorkshop_Worksheet.docx.

## Slide 2
2.4 Boolean logic | Lesson 3
Revise 360
By the end of this lesson
How do you create logic diagrams from truth tables?
1
Understand how to create, complete or edit logic diagrams and truth tables for given scenarios
Key words
Scenario
Logic diagram
Truth table
Intermediate output
AND
Notes: Share the objectives, then go straight into the starter. Devices stay away for the first five minutes.

## Slide 3
2.4 Boolean logic | Lesson 3
Revise 360
STARTER
Five minutes, on paper
A security light should come on when it is dark AND movement is detected, unless the test switch is on. Write that rule in your own words, then underline the logic words.
No devices yet. Write your answer on the worksheet before anyone talks.
Notes: Silent start. Take two or three answers before moving on: this is where misconceptions surface.

## Slide 4
2.4 Boolean logic | Lesson 3
Revise 360
Into the experience
Open Circuit workshop on revise360.co.uk
1
Look around
Six numbered stations are arranged around you. Turn right for 1 and 2, around for 3 and 4, left for 5 and 6.
2
Read, then write
Read the wall, write the key fact and your answer to the challenge on the worksheet.
3
Then tap the badge
Only answer the questions once you have written. Your first answer is the one that counts.
4
Look down at the end
The starred final challenge is on the floor. Predict on paper first.
Notes: Insist on writing before tapping. That single rule is the difference between revision and a quiz game.

## Slide 5
2.4 Boolean logic | Lesson 3
Revise 360
Station 1
1
From words to logic
Find the inputs and the output in the scenario.
Look for the words 'and', 'or', 'not', 'either' and 'regardless'.
Decide which parts go in brackets, then build from the inputs to the output.
CHALLENGE
How do you create a logic diagram from a scenario?
On your worksheet: To turn a scenario into logic...
Notes: Station 1: From words to logic. Students read this wall in the experience, write the key fact and the challenge answer, then answer the questions at the badge.

## Slide 6
2.4 Boolean logic | Lesson 3
Revise 360
Station 2
2
Scenario 1: the shop alarm
A shop alarm sounds (X) if the door sensor is triggered (A) AND the shop is closed (B).
Whatever the sensors say, it always sounds if the panic button is pressed (C).
CHALLENGE
Build the shop alarm circuit, then complete its truth table.
On your worksheet: The shop alarm expression is...
Notes: Station 2: Scenario 1: the shop alarm. Students read this wall in the experience, write the key fact and the challenge answer, then answer the questions at the badge.

## Slide 7
2.4 Boolean logic | Lesson 3
Revise 360
Station 3
3
Scenario 2: the hospital lift
A hospital lift has two doors (A and B). An alarm sounds (X)...
if either door is still open,
AND either the lift is moving (C) OR it is overloaded (D).
CHALLENGE
Why do both halves of this circuit use OR gates?
On your worksheet: The hospital lift expression is...
Notes: Station 3: Scenario 2: the hospital lift. Students read this wall in the experience, write the key fact and the challenge answer, then answer the questions at the badge.

## Slide 8
2.4 Boolean logic | Lesson 3
Revise 360
Station 4
4
Scenario 3: the greenhouse
A greenhouse heater runs (X) if the gardener switches it on (A) OR the timer starts it (B).
A window sensor (C) normally sends 0.
When a window is opened it sends 1, and the heater must switch off.
CHALLENGE
Why does the window sensor need a NOT gate?
On your worksheet: The greenhouse expression is...
Notes: Station 4: Scenario 3: the greenhouse. Students read this wall in the experience, write the key fact and the challenge answer, then answer the questions at the badge.

## Slide 9
2.4 Boolean logic | Lesson 3
Revise 360
Station 5
5
Editing a diagram
Sometimes a diagram needs changing to match a new rule.
Check each gate against the scenario, one at a time.
Test your change with a truth table.
CHALLENGE
The shop alarm should now need the panic button AND the shop to be closed. How would the circuit change?
On your worksheet: To edit a logic diagram...
Notes: Station 5: Editing a diagram. Students read this wall in the experience, write the key fact and the challenge answer, then answer the questions at the badge.

## Slide 10
2.4 Boolean logic | Lesson 3
Revise 360
Station 6
6
Reading diagrams
To write an expression from a diagram, start at the output and work backwards.
Each gate becomes an operator, and each gate feeding another becomes brackets.
CHALLENGE
Write the expression for the diagram in the experience.
On your worksheet: To write an expression from a diagram...
Notes: Station 6: Reading diagrams. Students read this wall in the experience, write the key fact and the challenge answer, then answer the questions at the badge.

## Slide 11
2.4 Boolean logic | Lesson 3
Revise 360
CHECK
Hands down. Everyone commits.
In the hospital lift, when does the alarm sound?
A
Only when both doors are open
B
Whenever the lift moves
C
Never
D
When at least one door is open, and the lift is either moving or overloaded
Notes: The answer is D: When at least one door is open, and the lift is either moving or overloaded. Do not say it yet. Every pupil commits first - fingers, whiteboards or a show of hands on each letter in turn - and you count the split before anyone can change their mind. IF MOST OF THE CLASS IS RIGHT: say why it is right in one sentence and go straight on to the independent work. IF A SIGNIFICANT GROUP IS ON ONE WRONG LETTER: that option is the misconception to teach against before anyone goes on. Go back to station 3, Scenario 2: the hospital lift, and work through its example again, aloud, with the class watching, then re-ask this question. The course's own response to a wrong answer here: Both OR gates must output 1. A limitation, stated rather than papered over: one response covers every wrong option; it does not say what to revisit for each one. The course does not record what each separate wrong option means, and this slide does not invent it. Decide your own reteach for each option before the lesson; the options above are the start of it. This is a real activity from the experience (bl-l03-s3-c2), so the wording here is the wording a pupil will see.

## Slide 12
2.4 Boolean logic | Lesson 3
Revise 360
★ FINAL CHALLENGE
Design and test
A security light turns on (Q) if it's dark (A) AND movement is detected (B), unless the test switch (C) is on. Build it, then complete its truth table.
Predict on paper first, then look down and test it.
Notes: Make them commit to an answer on paper before they tap the star. Guessing first costs them the learning.

## Slide 13
2.4 Boolean logic | Lesson 3
Revise 360
Worth knowing
The information markers dotted around the room
Logic in everyday rules
Nearly every automatic device hides a logic expression: a boiler, a lift, a car alarm. Reading the rule and underlining the words and, or and not is most of the work.
Real alarms
Burglar alarms really are built from logic like this, often with extra inputs for doors, windows and a timer.
Fail-safe design
Emergency stops are usually wired so that a broken wire also stops the machine. Safety engineers call this fail-safe design.
Programmable logic
Factories use programmable logic controllers (PLCs), which are programmed with logic diagrams very like the ones you're drawing.
Notes: Use these as a settler, or as something for early finishers to read in the experience.

## Slide 14
2.4 Boolean logic | Lesson 3
Revise 360
Exam practice
Devices away. Answer from memory on the worksheet.
A fire door alarm sounds (Q) when the door is open (D) AND the building is locked (L), or when the test button (T) is pressed. Write the Boolean expression.
[2]
Draw the logic diagram for your expression.
[3]
Notes: Timed and silent. Mark against the answer sheet, then ask students to record their weakest area.

## Slide 15
2.4 Boolean logic | Lesson 3
Revise 360
Before you go
Rate yourself on each of these
Creating diagrams for scenarios
Secure
Revise
Focus here
Completing truth tables with intermediate outputs
Secure
Revise
Focus here
Editing and reading logic diagrams
Secure
Revise
Focus here
Anything marked Focus here: reopen Circuit workshop and use review mode on the questions you got wrong.
Notes: Students copy their score-screen breakdown onto the worksheet, then rate themselves here.